Turbulent flow over square cylinder at Re=22,000

---
Setup
- 3 grids (768x768x4, 768x768x24, 768x768x64)
- D = 64 (8.3% blockage)
- 1,000,000 time steps
- No local grid refinements
- MRT collision
- Smagorinsky SGS model (Cs = 0.02)
- No wall functions/damping
- Run on 2 GPUs (~12hrs for largest grid)

---
Results
Force coefficients and recirculation length
	CD	CL'	St	Lr
Present (z=4)	1.70	1.12	? (need FFT)	1.08
Present (z=24)	2.23	1.29	0.136	1.16
Present (z=64)	2.14	1.34	0.132	0.83
Bouris (1999) (2D LES)	2.18	1.62	0.134	~0.5
Nakayama (2002) (3D LES)	2.20	1.236	0.135	1.28
Lyn 1995 (experiment)	2.1	-	0.132	1.38

---
Results
Mean stream-wise velocity (v/U)
Bouris, 1999

---
Results
Total fluctuating kinetic energy (k=0.5(u'u'+v'v'))
Bouris, 1999

---
Conclusions and outlook
- Inconclusive whether the increased span-wise dimension improves the results
- Grid refinements for LES is under development

---
References
- Bouris, D. and Bergeles, G. “2D LES of vortex shedding from a square cylinder”, Journal of Wind Engineering and Industrial Aerodynamics 80, pp 31-46, 1999
- Nakayama, A. and Vengadesan, S.N. “On the influence of numerical schemes and subgrid-stress models on large eddy simulation of turbulent flow past a square cylinder”, International Journal for Numerical Methods in Fluids, 38:227-253, 2002